## Slide 1
Workshop Day 1: software familiarization, forecast weather and oceanographic conditions, software feasibility.
Briefing
Chalmers University of Technology
April 5th, 2022

## Slide 2
State-of-the-art of the weather ship routing (WSR) systems
Inventory of grid & path-finding algorithms  most suitable algorithm
Model implementation
Feasibility of the software
Briefing

## Slide 3
State-of-the-art of the weather ship routing (WSR)
Wide academic research on long distances  meteorological forecasts for oceans
Little study on short distances  dimensional resolution of weather scripts
Intention of EU to move freight from road to sea, in order to reduce external costs through the promotion of multimodal transport chains

## Slide 4
Inventory of grid
Nodal connection possibilities
Grid refinement
Dijkstra & A* algorithms
Notes: These algorithms are applied at gridded scheme where each node is connected to a set of vicinity points.
The edges connecting nodes displayed by arrows for 4 different schemes: 4, 8, 16 and 24 edges. Each arrow represents potential ship courses or directions. Different grid resolution has been tested that a minimum 16 edges are required for the software.

## Slide 5
Inventory of different optimization path-finding algorithms  Dijkstra & A*
Same results have been obtained using both algorithms
Computational time reduction in a 60%

## Slide 6
Model implementation
The wave predictions used are provided by the Copernicus website.
The optimum route suggests sailing northward than minimum distance route.
The travel time reduction 15% of the total time.

## Slide 7
Temporal sequence of the snapshot of the Tunis – Nice route
Model implementation
Temporal sequence of the snapshot of the Tunis – Nice route (the optimal route magenta and the minimum distance route in yellow)

## Slide 8
c) Model implementation
Mannarini (inspired by Bowditch)
Aertssen
Khokhlov (suggested by Lubkovsky)

## Slide 9
Mannarini (inspired by Bowditch): final speed is computed in function of the non-wave affected speed () plus a reduction in function of the wave parameters.
 | (in kn/ft2)
0º≤ ≤45º | 0.0083
45º< <135º | 0.0165
135º≤ ≤225º | 0.0248
225º< <270º | 0.0165
270º≤ ≤360º | 0.0083
 | 0.0083
 | 0.0165
 | 0.0248
 | 0.0165
 | 0.0083
is an angle off bow with respect to vessel’s heading direction measured

## Slide 10
Aertssen: this formula includes ship dimensions (LBP) in speed reduction in function of waves parameters.
 |  |  | 150º-210º |  | 60º-150º 210º - 300º |  | 30º-60º 300º-330º |  | 0º-30º 330º-360º | 
BN | Hs | Wspeed | m | n | M | n | m | N | m | n
5 | 2.5 | 17-21 | 900 | 2 | 700 | 2 | 350 | 1 | 100 | 0
6 | 4.0 | 22-27 | 1300 | 6 | 1000 | 5 | 500 | 3 | 200 | 1
7 | 5.5 | 28-33 | 2100 | 11 | 1400 | 8 | 700 | 5 | 400 | 2
8 | 7.5 | 34-40 | 3600 | 18 | 2300 | 12 | 1000 | 7 | 700 | 3
 |  |  | 150º-210º |  | 60º-150º 210º - 300º |  | 30º-60º 300º-330º |  | 0º-30º 330º-360º | 
BN | Hs | Wspeed | m | n | M | n | m | N | m | n
5 | 2.5 | 17-21 | 900 | 2 | 700 | 2 | 350 | 1 | 100 | 0
6 | 4.0 | 22-27 | 1300 | 6 | 1000 | 5 | 500 | 3 | 200 | 1
7 | 5.5 | 28-33 | 2100 | 11 | 1400 | 8 | 700 | 5 | 400 | 2
8 | 7.5 | 34-40 | 3600 | 18 | 2300 | 12 | 1000 | 7 | 700 | 3

## Slide 11
Khokhlov (suggested by Lubkovsky): this formula takes into account vessels’ DWT and waves characteristics to calculate ship speed reduction.
Khokhlov method is applicable for:
Vessels from 4.000 to 20.000 DWT
Design speeds in between 9 and 20 knots.

## Slide 12
BBF
Case study
3 routes, 5 ports
From calm waters to waves 8 meters high.
Bowditch, Aertssen and Khokhlov formulas

## Slide 13
Speed reduction related to wave height and hitting angle variation based on Bowditch formulation
Case study

## Slide 14
Speed reduction related to wave height and hitting angle variation based on Aertssen formulation
Case study

## Slide 15
Speed reduction related to wave height and hitting angle variation based on Khokhlov formulation
Case study

## Slide 16
Case study

## Slide 17
Feasibility of the software
4 routes have been analysed, related to 5 ports and leaving from Barcelona.
Different speeds and weather conditions were selected to check its feasibility previously in Balearic and Italy, routes.

## Slide 18
Feasibility of the software
 | 10 knots | 16 knots | 22.6 knots | 30 knots
Calm-Smooth (0-0.5m) | No | No | No | No
Moderate-Rough (1.25 – 4m) - (FS) | No | No | No | No
Moderate-Rough (BS) | ½ | ½ | No | No
Moderate-Rough (HS) | ½ | ½ | No | No
Rough-High (FS) (4-9m) | Yes | Yes | ½ | ½
Rough-High (BS) | Yes | Yes | ½ | ½
Rough-High (HS) | Yes | Yes | Yes | Yes
FS (Following seas); BS (Beam seas); HS (Head seas). Yes (feasible); No (not feasible); ½ (not all the studied cases are feasible)